## Slide 1: Southern Spectroscopic Survey Instrument: Programmatics Josh Frieman, Fermilab & U. Chicago Jeff Newman, U. Pittsburgh/PITT PACC

## Slide 2: Context
2015: NSF-commissioned NRC “A Strategy to Optimize the US Optical and Infrared System in the Era of LSST” (Elmegreen report) recommended wide-field, highly multiplexed spectroscopy on intermediate-to-large aperture telescope in the southern hemisphere.
2016: DOE-commissioned “Cosmic Visions Dark Energy” (Dodelson report) identified a Southern Spectroscopic Survey facility as enhancing LSST science and one of several possible projects that could go beyond Stage IV DE experiments.
2016: NOAO-Kavli-LSST community study “Maximizing Science in the Era of LSST” report due out soon, will recommend wide-field, highly multiplexed optical spectroscopy on 8m+ telescope preferably in southern hemisphere.

## Slide 3: A Few Observations
Close coupling of photometric and WF spectroscopic surveys pays enormous scientific dividends: SDSS, DES/OzDES, KiDS/2dFLens, HSC/PFS, SDSS+DeCALS+DES/DESI,…, LSST/???
LSST is a fast, deep, wide survey. Spectroscopic resources are/will be in place for fast & deep spectroscopic follow-up.
Tremendous amount of (cosmic) science would be enabled by wide, multi-mega to giga-target spectroscopy of LSST objects: 3D map of ½ the sky. Follow CMB to the cosmic variance limit.
In general, for efficient (i.e., time-limited) multi-object surveys, need spectroscopic aperture ≥ photometric aperture (thousands vs few photons at mag limit for medium-res spectroscopy).
What follows are unendorsed personal views, and some numbers are at best educated guesses.

## Slide 4: Programmatics
Explore constrained, multi-dimensional trade space of:
        Telescope+instrument desiderata/design
           aperture, #fibers, λ range and resolution, FOV
    Cost
    Costs for fiber-fed (prime-focus) spectrographs primarily driven by fibers/positioners and spectrographs—relatively weak scaling with telescope aperture. DESI: 5000 fibers on 4m: ~$75M; PFS: 2400 fibers on 8m: ~$65M
    Timescales (construction, operation, funding)
    Science capabilities/goals (previous talks)
    Resource availability (may trump all others)
    Partner/stakeholder interests (agencies, communities,
    international)

## Slide 5: Agency Issues
DOE is a mission-driven agency that builds & operates experiments with well-defined science goals and requirements. In our case, this means cosmic frontier science as (narrowly) described in the P5 report. It does not fund astronomy.
Traditionally, astronomers have built multi-purpose facilities/instruments that enable a broad mix of science programs.
Multiple funding/partnership models possible, e.g.,:
  Time in exchange for instrument on existing telescope (e.g., DES)
  More time in exchange for instrument + telescope operations costs (e.g., DESI)
  Interagency or public-private partnership for new facility (e.g., LSST, SDSS)

## Slide 6: Blanco telescope, Chile
Same telescope used for DES: 4m diameter, currently w/ 3 deg2 FOV
  Successful experience with DOE/NSF/NOAO partnership
Clone or move DESI: 5000x multiplexing, ~7 deg2 FOV
  ~few M$ for move or ~60M$ for clone
DESpec: 5000x, 3 deg2 FOV with existing corrector, interchangeable w/ DECam:
~40M$

## Slide 7: Blanco telescope, Chile
Pros:
  Largest field of view w/ DESI move or clone
  Moving DESI cheapest option for an SSSI; mid-2020s possible
Cons:
  Small aperture requires long survey times
  Earthquake safety of DESI corrector?
  Kavli/NOAO/LSST report will recommend DECam stay on Blanco at minimum 3 years into LSST survey; would delay SSSI deployment unless DESpec option

## Slide 8: Magellan telescope, Chile
Two 6.5 diameter telescopes
Potential f/3 secondary would match DESI input beam and enable 1.5-2 deg diameter field of view with 3000-6000 positioners
New secondary would cost ~$few M million, plus ~$75M+(?) for instrument
Magellan institutions with majority of time interested in partnership: successful model with SDSS4/APOGEE-South
  SSSI instrument could form the basis of a SDSS6 survey; potential public/private partnership

## Slide 9: Magellan telescope, Chile
Pros:
  Larger collecting area
  Existing telescope makes earlier schedule possible: mid-2020s?
Cons:
  Would prefer even larger aperture, >8m (Kavli/NOAO/LSST)
  If use an existing Magellan telescope, must navigate politics of Magellan institutions, time access likely limited.
Build a 3rd Magellan telescope for this? Add $75M+ and additional construction time.

## Slide 10: Gemini telescope, Chile
8m telescope, US(NSF)-led international consortium
Current FOV is small
With ~$50M upgrade, could get 1.5 deg FOV, plus ~$75M instrument: WFMOS redux.
Pros:
  Larger collecting area; US-led
Cons:
  Total cost >~$125M
  Gemini-South desired lead role in LSST transient follow-up. Probably not available before late 2020s.
Gemini-North might be more available, but in wrong hemisphere.

## Slide 11: Mayall Telescope, Arizona
4m diameter
Latitude 32N
Could use (possibly upgraded) DESI instrument from mid-2020s
Pros:
  Enables SSSI science without new instrument
Cons:
  Northern hemisphere, can access only ½ of LSST area
  Very large amounts of time required to do SSSI program on 4m
  Gets worse at the higher airmasses required to reach into LSST footprint from Kitt Peak

## Slide 12: Telescopio San Pedro Mártir, Mexico
Magellan clone, 6.5m diameter
Latitude 30N
Might begin construction 2017 (finish FY23), funding decision imminent
$74M projected telescope budget, plus ~$75M+(?) for instrument
Pros:
  Simpler politics than Magellan, enthusiasm of partners to host an SSSI-like instrument
Cons:
  Northern hemisphere
  Smaller than some other options
  Not yet certain to be built, time access likely limited.

## Slide 13: Subaru (+PFS spectrograph), Hawai'i
8m diameter, wide-field telescope
PFS spectrograph, 2400 fibers over 1.3 deg, under construction, commissioning to be completed 2019
Pros:
  Enables SSSI without new instrument
Cons:
  Northern hemisphere, but can access majority of LSST footprint
  Limited time access: must compete with other Japanese priorities and potential time allocations for WFIRST
  Subaru relatively expensive to build + operate

## Slide 14: Keck (+FOBOS spectrograph), Hawai'i
10m diameter, narrower-field telescope
FOBOS: proposed 500-object spectrograph
Designed for high efficiency: could have comparable survey speeds to PFS
Pros:
  Large telescope aperture
  Could enable kinematic weak lensing via mini-IFUs
Cons:
  Northern hemisphere, but accesses majority of LSST footprint
  Very limited multiplexing and FOV
  Limited time available: largest Keck programs to date have been ~100 nights

## Slide 15: Mauna Kea Spectroscopic Explorer, Hawai'i
11m diameter telescope with 1.5 degree field of view, replacing CFHT
Designed solely for spectroscopy with an SSSI-like (3200-fiber) instrument
Pros:
  Large aperture, wide field, very high survey speed
  Enthusiastic about collaborating
Cons:
  Northern hemisphere, but accesses majority of LSST footprint
  Not yet funded; timescale?
  Cost to join: $50 million (in-kind via instrument construction?)
Note: similar telescope concepts for South under ESO discussion.

## Slide 16: New 8m WF Telescope in Chile
Strawman 8m+ telescope with >1.5 degree field of view
Designed ab initio for WF, highly multiplexed spectroscopy
Pros:
  Large aperture, wide field, very high survey speed, access, LSST overlap
Cons:
  Cost and timescale?

## Slide 17: Budget scenarios
~$5-10M:
  Upgrade DESI in North, or upgrade and move to South
~$40M:
  DESpec on Blanco
~$75M+:
  New instrument for existing or funded 6-10m telescope
  Join existing or planned facility (PFS, MSE,…)
  ~$125-150M+:
  New instrument on upgraded Gemini
  ~$250M+:
  New instrument on new 8m+ in the south
  Large uncertainties in the larger numbers, depending on design details, partnership arrangements, etc.
  DES and DESI were/will be ~10 yrs from conception to survey start. LSST ~25 yrs. More ambitious projects will be on-sky well after mid-2020s.

## Slide 18: Potential Partners
Astronomy community has identified SSSI-like instrument as a priority, but will want to enable non-cosmic science.
NASA could be interested in partnering for WFIRST photo-z training/calibration?
Private consortia with existing or to-be-built 6-10m telescopes may be interested in partnering for cash or instrument.
The international community also recognizes and is discussing the potential benefits for such a capability in the LSST era. International partnerships possible and may be necessary for larger-scale implementations of SSSI.